## Slide 1: Backend Methods for Visual SLAM
Zhang Handuo
ST Engineering-NTU Corporate Laboratory
School of Electrical and Electronic Engineering Nanyang Technological University
3 August 2018

## Slide 2
Outline
Introduction
Preliminaries
  Camera Model
  Visual Odometry
Backend Methods
  EKF
  Bundle Adjustment
  Sparsity
  Marginalization
QA

## Slide 3
Application
SLAM: Simultaneous Localization and Mapping
Augmented Reality (AR)
Visual Servo
Intelligent Hardware
Autonomous Driving
1. Introduction

## Slide 4
Camera Sensor (visible spectrum) Passive sensor
Pros :
  Provide abundant meaningful information (color, texture, shape…)
  Low price
  Light weight
Cons :
  Strong environment assumptions
  Large amount of calculation
  Numerical instabilities, ill-conditioned problems, image noise
Laser Sensor Active sensor
Pros :
  Accurate
  Fast
  Calculation amount smaller
Cons :
  Large in size
  High power consumption
  High price
1. Introduction
Sensor
Interoceptive sensors: IMU, wheel encoder, cameras, etc.
Exteroceptive sensors: GPS, artificial markers, etc.
Notes: Assumptions: sufficient illumination, dominance of static scene over moving objects, enough texture to allow apparent motion to be extracted, sufficient scene overlap between consecutive frames

## Slide 5
1. Introduction
Low cost
No range limitation
Acquire depth
No range limitation
Active acquire depth
Better reconstruction
Small detection range
Complex configuration
Complex calculation
Scale uncertainty
Initialization issue
Small detection range
Sensitive to material textures
Monocular
Stereo
RGB-D
Sensor
Notes: Assumptions: sufficient illumination, dominance of static scene over moving objects, enough texture to allow apparent motion to be extracted, sufficient scene overlap between consecutive frames

## Slide 6
1. Introduction
SFM
1. Introduction
Definition
VSLAM
VO
Input: unordered image sets
Output: 6DOF pose and 3D reconstruction
Local consistency
Global consistency
Input: sequential camera frames
Output: 6DOF pose estimation of camera

## Slide 7
1. Introduction
SFM: Structure from Motion
Snavely, N., Seitz, S. M., & Szeliski, R. (2006, July). Photo tourism: exploring photo collections in 3D. In ACM transactions on graphics (TOG) (Vol. 25, No. 3, pp. 835-846). ACM.
1. Introduction
SFM

## Slide 8
1. Introduction
Sense the environment
Know where I am w.r.t. initial place
Unknown initial location
Unknown Environment
Internal State Estimation
Surrounding Perception
Mapping
Calculate 6D pose
Construct model and optimize to eliminate noises
1. Introduction
VSLAM

## Slide 9
1. Introduction
Challenges
1. Introduction
VSLAM
No prior knowledge
Real-time
Long-term travelling (Drift, memory usage)
Robustness to sudden environment change (illumination, scale, motion)
Dynamic environment
Sensor fusion
Mapping (integrates with navigation and reconstruction)

## Slide 10
Front-end is responsible for:
Feature extraction, matching, outlier removal
Loop closure detection
Back-end is responsible for:
Pose and structure optimization (g2o, Ceres, GTSAM)
1. Introduction
VSLAM

## Slide 11
2. Preliminaries
1. Mathematical Formulation of Visual SLAM
A mobile robot moves in unknown environment, modeled as a collection of M static landmarks. Given a set of visual measurements , the task is to estimate the landmark positions and sequence of poses .
Sequence of poses generate a trajectory:
Landmarks that can be observed:
Motion Model:
Observation Model for landmark :
2. Classic SLAM Solution: Probabilistic Modeling
How to estimate?
Maximum a posteriori (MAP) estimate

## Slide 12
  2.1 Camera Model
2. Preliminaries
Camera Coordinate
Image Coordinate
Normalized Coordinate
Normalized Plane
Image Coordinate
p
z
yc
xc
Oc
P

## Slide 13
  2.1 Camera Model
2. Preliminaries
Camera Coordinate
Image Coordinate
Normalized Coordinate
Normalized Plane
Image Coordinate
p
yc
xc
Oc
P
Global Coordinate
yg
xg
zg
zc

## Slide 14
  2.2 Visual Odometry
2. Preliminaries
Feature based Visual Odometry
2. Minimize the Reprojection error
1. Extract & match features (+RANSAC)

## Slide 15
  2.2 Visual Odometry
2. Preliminaries
Direct Image Alignment
Minimize the per-pixel intensity difference — photometric error
Dense: DTAM [Newcombe et al. `11] 300,000+ pixels
Semi-Dense: LSD-SLAM [Engel et al. `14] 10,000 pixels
Sparse: SVO [Forster et al. `14] 2,000 pixels

## Slide 16
  2.2 Visual Odometry
2. Preliminaries
Monocular SLAM Initialization — 2D-to-2D correspondences [1]
Epipolar constraint
Eight-point algorithm
Five-point algorithm
DLT method
SVD
[1] Scaramuzza, D., & Fraundorfer, F. (2011). Visual odometry [tutorial]. IEEE robotics & automation magazine, 18(4), 80-92.
Limitation
Scale ambiguity
Pure rotation issue

## Slide 17
  2.2 Visual Odometry
2. Preliminaries
3D-to-2D correspondences
Perspective-n-Point (PnP):
DLT
P3P
Efficient PnP
UPnP

## Slide 18
3. Backend
Recall
Sequence of poses generate a trajectory:
Landmarks that can be observed:
Motion Model:
Observation Model for landmark :
Probabilistic Modeling
Maximum a posteriori (MAP) estimate

## Slide 19
3.1 EKF
3. Backend
Main idea
Linearize measurement functions at linearization point and use Gaussian distribution to approximate the nonlinear noises.
Predict - Update Kalman filter processes.
Limitation
Markov property assumption. So if the current frame is related to historical data (loop closure), the filter fails.
EKF is implemented by linearizing the observation model. High-order item was abandoned and the linearization point is only an estimated value, which leads to inconsistency.
Quadratic cost both in storage and update time.

## Slide 20
3.2 Bundle Adjustment
3. Backend
MAP Inference for Nonlinear Factor Graphs

## Slide 21
3.2 Bundle Adjustment
3. Backend
MAP Inference for Nonlinear Factor Graphs
Map points
Local BA
Global BA
Marginalization

## Slide 22
3.2 Bundle Adjustment
3. Backend
MAP Inference for Nonlinear Factor Graphs
Assume measurement follow Gaussian distribution
Measurement equation：
Error function
Minimizing cost function such that
Least Squares Optimization Problem [2]
[2] Grisetti, G., Kummerle, R., Stachniss, C., & Burgard, W. (2010). A tutorial on graph-based SLAM. IEEE Intelligent Transportation Systems Magazine, 2(4), 31-43.

## Slide 23
3.2 Bundle Adjustment
3. Backend
Linearization
Initial guess
measurement Jacobian of
state update vector
whitened Jacobian matrices
Information matrix
[3] Kümmerle, R., Grisetti, G., Strasdat, H., Konolige, K., & Burgard, W. (2011, May). g 2 o: A general framework for graph optimization. In Robotics and Automation (ICRA), 2011 IEEE International Conference on (pp. 3607-3613). IEEE.

## Slide 24
Parametrization
Camera Poses
3D Landmarks
: 3D position
Euclidean XYZ Param:
: 6D state vector
Inverse Depth Param [4]:
[4] Civera, J., Davison, A. J., & Montiel, J. M. (2008). Inverse depth parametrization for monocular SLAM. IEEE transactions on robotics, 24(5), 932-945.
Euclidean Space: | ,
Special Euclidean Space: | SO(3),
Rigid body rotation constraints
To cope with easier optimization
3. Backend
Lie Group
SO(3)
Lie Algebra

## Slide 25
Parametrization
Camera Poses
Special Euclidean Space: | SO(3),
3. Backend
Lie Group
SE(3):
Lie Algebra
:
=
Linearization --- Perturbation model [5]
is the corresponding lie algebra of perturbation
[5] Barfoot, T. D. (2017). State Estimation for Robotics. Cambridge University Press.
)

## Slide 26
3D Landmarks
[4] Civera, J., Davison, A. J., & Montiel, J. M. (2008). Inverse depth parametrization for monocular SLAM. IEEE transactions on robotics, 24(5), 932-945.
Parametrization
3. Backend
: 6D state vector
Inverse Depth Param [4]:

## Slide 27
3.2 Bundle Adjustment
3. Backend
State update
Initial guess
measurement Jacobian of
state update vector
composition on manifold
Represents perturbation
Gauss-Newton method
Levenberg-Marquardt method (Trust region method)
Powell’s dogleg algorithm
Iterative Optimization methods
Off the shelf package: g2o, gtsam, ceres

## Slide 28
3.2 Bundle Adjustment
3. Backend
Inside each iteration
Cholesky Factorization --- CHOLMOD, CXSParse
QR Factorization --- SPQR, Eigen QR module

## Slide 29
3. Backend
Jacobian matrix - Partial derivative of F w.r.t camera pose
Jacobian matrix - Partial derivative of F w.r.t landmark position
3.2 Visual SLAM BA
3D point in camera coordinate

## Slide 30
3. Backend
3.3 Sparsity
=

## Slide 31
3. Backend
3.3 Sparsity
J =
=

## Slide 32
3. Backend
3.3 Sparsity
J =
=
=

## Slide 33
3. Backend
3.3 Sparsity
J =
=
=

## Slide 34
3. Backend
Schur Complement [6]
[6] Sibley, G., Matthies, L., & Sukhatme, G. (2010). Sliding window filter with application to planetary landing. Journal of Field Robotics, 27(5), 587-608.
The second row is eliminated to obtain the Schur complement that involves only .
3.3 Sparsity

## Slide 35
3.4 Marginalization
3. Backend
Sliding Window
separator
Variable to be marginalized
Variable related
Follow equation 16

## Slide 36
3.4 Marginalization
3. Backend
First Jacobian Estimation [7]:
[7] Huang, G. P., Mourikis, A. I., & Roumeliotis, S. I. (2009). A first-estimates Jacobian EKF for improving SLAM consistency. In Experimental Robotics(pp. 373-382). Springer Berlin Heidelberg.
For , we fix the linearization point and no longer use updated to get Jacobian.
Follow equation 17

## Slide 37
Elimination Order:
[8] Kaess, M., Johannsson, H., Roberts, R., Ila, V., Leonard, J. J., & Dellaert, F. (2012). iSAM2: Incremental smoothing and mapping using the Bayes tree. The International Journal of Robotics Research, 31(2), 216-235.
[9] Frank Dellart, Michael Kaess. (2017). Factor Graph for Robot Perception.

## Slide 38
3.5 Pose-only BA
3. Backend

## Slide 39
Q&A